## Slide 2: Boolean Functions

## Slide 3: Boolean Functions
A Boolean function is an expression formed with binary variables, the two binary operators OR and AND, the unary operator NOT, parenthesis and equal sign.
Venn diagram is used to visualize the relationships among the variables of a Boolean expression.
Boolean function can be expressed in algebraic expression or truth table.

## Slide 4: Boolean Function Repressentation(Truth Table)
z
x
y
x
F4
x
z
y
x
z
y
x
F3
x
F2
+
=
+
=
=
y
z
+
y
+
xy
F1
=
z
Implement the above expression using logic gates.

## Slide 5: Canonical Forms and Standard Forms

## Slide 6: Canonical Forms
In Boolean algebra Boolean functions are expressed in a forms:
  Canonical Forms
  Standard Forms
Canonical Forms in common usage:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)

## Slide 7: Minterms and Maxterms
Min terms are AND terms with every variable present in either true or complemented form. Minterms are also referred as standard product
N variables forming an OR term, with each variable being primed or unprimed, provide 2n possible combinations, called maxterms or standard sums.

## Slide 8: Minterms and Maxterms for three binary variables
 |  |  | Minterms |  | Maxterms | 
X | Y | Z | Term | Designation | Term | Designation
0 | 0 | 0 | x′y′z′ | m0 | x + y + z | M0
0 | 0 | 1 | x′y′z | m1 | x + y + z′ | M1
0 | 1 | 0 | x′yz′ | m2 | x + y′ + z | M2
0 | 1 | 1 | x′yz | m3 | x + y′ + z′ | M3
1 | 0 | 0 | xy′z′ | m4 | x′ + y + z | M4
1 | 0 | 1 | xy′z | m5 | x′ + y + z′ | M5
1 | 1 | 0 | xyz′ | m6 | x′ + y′ + z | M6
1 | 1 | 1 | xyz | M7 | x′ + y′ + z′ | M7

## Slide 9: Boolean Functions
X | Y | Z | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Sum of min terms:-
F1 = x′y′z + xy′z′ + xyz = m1 + m4 + m7
= Σ(1,4,7)
F2 = x′yz + xy′z + xyz′ + xyz
= m3 + m5 + m6 + m7
= Σ (3, 5, 6, 7)
Product of Max terms:-
F1 = (x + y + z) (x + y′ + z) (x + y′ + z′) (x′ + y + z′) (x′ + y′ + z)
= M0.M2.M3.M5.M6
= Π (0,2,3,5,6)
F2 = (x + y + z) (x + y + z′) (x + y′ + z) (x′ + y + z)
= M0.M1.M2.M4
= Π (0, 1, 2, 4)

## Slide 10: Express as Canonical forms
F = A+ B’C in Sum of minterms
F = XY+X’Z in SOM & POM
F(A,B,C,D)=D(A’+B)+B’D (SOM & POM)
F(W,X,Y,Z)= Y’Z+WXY’+WXZ’+W’X’Z (SOM & POM)

## Slide 11: Conversion between canonical forms
Ex: F(A, B, C) = Σ (1,4,5,6,7)
F′(A, B, C) = Σ (0,2,3)
F(A, B, C) = Π (0,2,3)

## Slide 12: Boolean function
Represent the following sentence in different forms of Boolean equation
You should wear your overshoes if you are outside in a heavy rain and you are wearing your new suede shoes, or if your mother tells you to.

## Slide 13: Standard Forms
The terms that form the function may contain one, two or any number of literals.
Two types
  Sum of products
    Is a Boolean expression containing AND terms called product terms of one or more literals each
    Ex: F1 = y′ + xy + x′yz′
  Product of sums
    Is a Boolean expression containing OR terms, called sum terms.
    Ex: F2 = x(y′ + z)(x′ + y + z′ + w)