## Slide 1: Decoders and Encoders

## Slide 2: Decoder
Is a combinational circuit that converts binary information from n input lines to a maximum of 2n unique output lines.
n-to-m line decoders => n input lines, m ≤ 2n output lines.
Can also be used to convert codes
Outputs are mutually exclusive because only one output is enabled at any one time.

## Slide 3: 3 – to – 8 Line Decoders or Binary to Octal decoder

## Slide 4: Logic diagram of 3 x 8 Decoder

## Slide 5: Combinational logic Implementation using decoders
The outputs of the decoder are the minterms of the Boolean function.
So, decoders can be used to design of the combinational circuits with an external OR gate to form the sum.
Ex: full adder: Sum (x, y, z) = Σ(1, 2, 4, 7) Carry (x, y, z) = Σ(3, 5, 6, 7)

## Slide 6: Implementation of Full adder using decoders

## Slide 7: Decoder
A 2 – to – 4 line decoder with an enable input constructed with NAND gates and complemented outputs.

## Slide 8: Demultiplexer
A decoder with an enable input functions as a demultiplexer.
Demultiplexer is a circuit that receives information on a single line and transmits this information on one of 2n possible output lines.

## Slide 9: Decoder vs Demultiplexers

## Slide 10: 4 x 16 decoder using two 3 x 8 decoders

## Slide 11: Assignment
Design BCD – to – decimal decoder
Design a 5 x 32 decoder using 4 3 x 8 decoder and 1 2 x 4 decoder
Design a combinational circuit for the given maxterms 0,3,5,7
Design a full subtractor using decoder
Design 1:32 demultiplexer tree using 1:4 and 1:8 demux

## Slide 12: Encoders

## Slide 13: Encoders
Is a digital function that produces a reverse operation from that of a decoder.
An encoder has 2n (or less) input lines and n output lines.
Ex: Octal to Binary encoder

## Slide 14: Octal to Binary Encoder

## Slide 15: Logic diagram of Octal to Binary Encoder